## Slide 1
Segmentation of Bone Marrow on 18F-FDG PET/CT Images
Daniel Huff
CS 766, Spring 2018

## Slide 2: Background: PET/CT Imaging
CT – Computed Tomography
3D x-ray transmission imaging
Provides anatomical information
CT: sagittal view
FDG PET: coronal view
PET – Positron Emission Tomography
18F-FDG – distribution of glucose metabolism
Provides functional information

## Slide 3: Background: Quantitative Bone Marrow Analysis
Quantification FDG PET uptake of bone marrow is important for several diseases:
  Cancers that affect bone marrow
    Multiple Myeloma1
    Leukemia2
    Lymphoma3-5
  Oncology patients receiving immunotherapies6,7
Other researchers have addressed this problem, but with limitations:
  Perk et al (2016) – different radiotracer8
  Nguyen et al (2017) – vertebral marrow only, requires other manual inputs9
  Leydon et al (2016) – no consideration of separate vertebrae, manual inputs, other simplifications10
Currently, PET images are used semi-quantitatively due to the expert physician time commitment required for manual segmentation – automation can address this

## Slide 4: Methods: Outline
Whole Bone segmentation
Bone Marrow segmentation
  Vertebral marrow
  Other marrow

## Slide 5: Methods: Outline
Whole Bone segmentation
Bone Marrow segmentation
  Vertebral marrow
  Other marrow

## Slide 6: Methods: Whole Bone Segmentation
Input CT
Threshold high density regions
HU > 150
Morphological open, close
Remove table
Mask CT or PET with bone mask for whole bone segmentation

## Slide 7: Methods: Outline
Whole Bone segmentation
Bone Marrow segmentation
  Vertebral marrow
  Other marrow

## Slide 8: Methods: Vertebral Marrow Segmentation Localization of Shoulders and Pelvis
Strongest peaks at shoulders, pelvis
Axial sum of PET mask = measure of body x-sectional area

## Slide 9: Methods: Vertebral Marrow Segmentation Detection of Intervertebral Disks
Axial minima correspond to intervertebral disks
Detected minima (Red = CT, Green = PET)

## Slide 10: Methods: Vertebral Marrow Segmentation Erosion of Bone Mask Segments
Erosion of bone mask segments between adjacent minima
Final Vertebral Marrow Segmentation (Blue)
Detected minima (Red = CT, Green = PET)

## Slide 11: Methods: Outline
Whole Bone segmentation
Bone Marrow segmentation
  Vertebral marrow
  Other marrow

## Slide 12: Methods: Other Marrow Segmentation
Subtract vertebral marrow from whole bone mask
Erode hard bone
Union of vertebral, other marrow is final segmentation
Select largest components as other marrow
Input final vertebral marrow segmentation

## Slide 13: Sample Results: Final Marrow Segmentation
Sagittal
Coronal

## Slide 14: Sample Results: Vertebra Failure Possibilities False Positives
False positive disk location causes split vertebra segmentation
Most prevalent in L spine, where vertebra are tallest

## Slide 15: Sample Results: Vertebra Failure Possibilities False Negatives
Missed disk location leads to fused marrow segmentation
Most prevalent in C spine
  Vertebra are smaller
  Intervertebral disks may be a single voxel
  Vertebra may be tilted if patient is not supine

## Slide 16: Discussion: Moving Forward
Method performs reasonably in most of cohort of 30 patients
Current run time: 120 seconds/patient
Two planned improvements:
  Kalman filtering of intervertebral disk location for false positive rejection
  Transition to model-based approach11 to address multiple current issues:
    Incomplete bone segmentation
    Shoulder, pelvis localization
    Remove reliance on multiple engineered parameters

## Slide 17: Conclusions
Development of a simple framework for 3D segmentation of bone marrow on 18F-FDG PET/CT images
Future transition to a model-based approach should address some shortcomings of this approach
Applications for disease staging, treatment management, treatment response assessment for multiple diseases

## Slide 18: References
1 Sachpekidis, C., et al. "Assessment of glucose metabolism and cellular proliferation in multiple myeloma: a first report on combined 18 F-FDG and 18 F-5 FLT PET/CT imaging." EJNMMI research 8.1 (2018): 28.
2 Stölzel, Friedrich, et al. "18F-FDG-PET/CT for detection of extramedullary acute myeloid leukemia." Haematologica 96.10 (2011): 1552-1556.
3 Barrington, Sally F., et al. "Role of imaging in the staging and response assessment of lymphoma: consensus of the International Conference on Malignant Lymphomas Imaging Working Group." Journal of clinical oncology 32.27 (2014): 3048.
4 Berthet, Louis, et al. "In newly diagnosed diffuse large B-cell lymphoma, determination of bone marrow involvement with 18F-FDG PET/CT provides better diagnostic performance and prognostic stratification than does biopsy." Journal of Nuclear Medicine 54.8 (2013): 1244-1250.
5 Herrmann, Ken, et al. "Early response assessment using 3′-deoxy-3′-[18F] fluorothymidine-positron emission tomography in high-grade non-Hodgkin's lymphoma." Clinical Cancer Research 13.12 (2007): 3552-3558.
6 Ferté, Charles, and Aurélien Marabelle. "iRECIST: A clarification of tumour response assessment in the immunotherapy era." European Journal of Cancer 77 (2017): 165-167.
7 Seymour, Lesley, et al. "iRECIST: guidelines for response criteria for use in trials testing immunotherapeutics." The Lancet Oncology 18.3 (2017): e143-e152.
8 Perk, Timothy G., et al. "A method for quantitative total marrow imaging (QTMI) with PET/CT." Biomedical Physics & Engineering Express 2.5 (2016): 055006.
9 Nguyen, Chuong, et al. "An automatic 3D CT/PET segmentation framework for bone marrow proliferation assessment." Image Processing (ICIP), 2016 IEEE International Conference on. IEEE, 2016.
10 Leydon, P., et al. "Automatic bone marrow segmentation for PETCT imaging in multiple myeloma." Physica Medica: European Journal of Medical Physics 32 (2016): 242.
11 Yip, Stephen, Timothy Perk, and Robert Jeraj. "Development and evaluation of an articulated registration algorithm for human skeleton registration." Physics in Medicine & Biology59.6 (2014): 1485.

## Slide 19: Sample Results: Final Marrow Segmentation 2
Sagittal
Coronal